## Slide 1
DISCOVER . LEARN . EMPOWER
Batteries
UNIVERSITY INSTITUTE OF ENGINEERING
DEPARTMENT APPLIED PHYSICS
Bachelor of Engineering (Computer Science & Engineering)
Basics of Electrical & Electronics Engineering
ELT- 112
Er. Akhil Nigam

## Slide 2: BATTERY
Course Outcome
https://www.123rf.com/photo_71633945_stock-vector-simple-battery-scheme-the-illustration-shows-the-main-elements-of-battery.html
CO Number | Title | Level
CO1 | Students will be able to establish the equations that characterize the performance of an electric circuit as well as solving both single phase and three-phase AC circuits in sinusoidal steady state. | Remember
CO2 | Students will be made aware about the electrical safety and implementation of electric wiring. | Understand
CO3 | Introducing students to the areas of rotating electric machines, with application of motors in particular, transducers and electric batteries. | Understand
CO4 | Comprehension of different applications of Op-amps in electronic circuits and its interfacing with A/D-D/A converters.. | Understand

## Slide 3: BATTERY
A battery is a device that stores energy. The way that it stores energy is by holding different electro-chemically active materials together is such a fashion so that they can generate and store free electrons (electrical potential energy) for long periods of time and only deliver that energy when the battery user demands it.
https://www.123rf.com/photo_71587542_stock-vector-vector-dry-battery-diagram.html

## Slide 4: TYPES OF BATTERY
1.Primary cell
2.Secondary cell
Primary cell or battery:
One use (non-rechargeable/disposable)
Chemical reaction used, can not be reversed
Used when long periods of storage are required
Lower discharge rate than secondary batteries
Use:
smoke detectors, flashlights, remote controls.

## Slide 5: SECONDERY CELL
Rechargeable batteries
Reaction can be readily reversed
Similar to primary cells except redox reaction can be reversed
Recharging:
  Electrodes undergo the opposite process than discharging
  Cathode is oxidized and produces electrons
  Electrons absorbed by anode
https://en.wikipedia.org/wiki/Rechargeable_battery

## Slide 6: PRIMARY V/S SECONDARY BATTERY

## Slide 7: SPECIFICATIONS OF BATTERY
State of Charge (SOC) – An expression of the present battery capacity as a percentage of maximum capacity. SOC is generally calculated using current integration to determine the change in battery capacity over time.
Depth of Discharge (DOD) – The percentage of battery capacity that has been discharged expressed as a percentage of maximum capacity. A discharge to at least 80 % DOD is referred to as a deep discharge.
Terminal Voltage – The voltage between the battery terminals with load applied. Terminal voltage varies with SOC and discharge/charge current.
Open-circuit voltage – The voltage between the battery terminals with no load applied. The open-circuit voltage depends on the battery state of charge, increasing with state of charge.
Internal Resistance – The resistance within the battery, generally different for charging and discharging, also dependent on the battery state of charge. As internal resistance increases, the battery efficiency decreases and thermal stability is reduced as more of the charging energy is converted into heat.

## Slide 8: PARAMETERS OF BATTERY
Nominal Voltage (V) – The reported or reference voltage of the battery, also sometimes thought of as the “normal” voltage of the battery.
• Cut-off Voltage – The minimum allowable voltage. It is this voltage that generally defines the “empty” state of the battery.
• Capacity or Nominal Capacity (Ah for a specific C-rate) – The coulometric capacity, the total Amp-hours available when the battery is discharged at a certain discharge current (specified as a C-rate) from 100 percent state-of-charge to the cut-off voltage. Capacity is calculated by multiplying the discharge current (in Amps) by the discharge time (in hours) and decreases with increasing C-rate.
• Energy or Nominal Energy (Wh (for a specific C-rate)) – The “energy capacity” of the battery, the total Watt-hours available when the battery is discharged at a certain discharge current (specified as a C-rate) from 100 percent state-of-charge to the cut-off voltage. Energy is calculated by multiplying the discharge power (in Watts) by the discharge time (in hours). Like capacity, energy decreases with increasing C-rate.
• Cycle Life (number for a specific DOD) – The number of discharge-charge cycles the battery can experience before it fails to meet specific performance criteria. Cycle life is estimated for specific charge and discharge conditions. The actual operating life of the battery is affected by the rate and depth of cycles and by other conditions such as temperature and humidity. The higher the DOD, the lower the cycle life.
• Specific Energy (Wh/kg) – The nominal battery energy per unit mass, sometimes referred to as the gravimetric energy density. Specific energy is a characteristic of the battery chemistry and packaging. Along with the energy consumption of the vehicle, it determines the battery weight required to achieve a given electric range

## Slide 9: POWER SUPPLY AND LINEAR POWER SUPPLY
DC power supply is to supply clean DC voltage to these devices. DC power supplies are categorized into linear and switched-mode, which are the topologies involved to make AC mains supply into smooth DC. Linear power supply uses a transformer to directly step-down the AC mains voltage into a desired level while SMPS converts AC to DC using a switching device which helps to obtain an average value of the desired voltage level.
Linear power supply: In a linear power supply, the mains AC voltage is converted to a lower voltage directly by a step-down transformer. This transformer has to handle a large power since it works at the AC mains frequency 50/60Hz. Therefore, this transformer is bulky and large, making the power supply heavy and large.
Stepped-down voltage is then rectified and filtered to get the DC voltage required for the output. Since the voltage at this level is subjected to vary depending on the distortions of the input voltage, a voltage regulation is done before the output. The voltage regulator in a linear power supply is a linear regulator, which is usually a semiconductor device that acts as a variable resistor. The output resistance value changes with the output power requirement, making the output voltage constant. Thus, the voltage regulator operates as a power dissipating device.

## Slide 10: DIAGRAM OF LINEAR POWER SUPPLY
https://slideplayer.com/slide/3425797/

## Slide 11: SWITCHED MODE POWER SUPPLY
SMPS (switched-mode power supply) operates on a switching transistor device. At first, the AC input is converted to DC voltage by a rectifier, without reducing the voltage, unlike in a linear power supply. Then the DC voltage undergoes a high-frequency switching, typically by a MOSFETtransistor. That is, the voltage through the MOSFET is turned on and off by MOSFET Gate signal, usually a pulse-width-modulated signal of about 50 kHz (chopper/inverter block). After this chopping operation, the waveform becomes a pulsated-DC signal. After that, a step-down transformer is used to reduce the voltage of the high-frequency pulsated DC signal to the desired level. Finally, an output rectifier and a filter are used to make back the output DC voltage.
https://en.wikipedia.org/wiki/Switched-mode_power_supply

## Slide 12: APPLICATIONS OF BATTERY

## Slide 13: APPLICATION OF BATTERY

## Slide 14: APPLICATIONS
Zinc-Carbon batteries used in low power drain applications such as flash lights, remote control, toys, and table clocks.
Lead-acid batteries are starting, lightning, and ignition systems(SLI) of automobiles.
Lithium batteries are portable consumer instruments like calculators, iPods, digital diaries, wrist watches and stop watches, toys, and artificial pacemakers.
Lead acid batteries are used such as solar-panel energy storage, vehicle ignition and lights, backup power and load levelling in power generation/distribution.

## Slide 15: Assessment Pattern
S. No. | ELEMENTS | MARKS
1 | MST-1 | 36
2 | MST-2 | 36
3 | ASSIGNMENT (1+2+3) | 12
4 | SURPRISE TEST | 09
5 | TUTORIAL TEST | 09
6 | QUIZ | 12

## Slide 16: REFERENCES
https://www.123rf.com/photo_71633945_stock-vector-simple-battery-scheme-the-illustration-shows-the-main-elements-of-battery.html.
https://www.123rf.com/photo_71587542_stock-vector-vector-dry-battery-diagram.html
https://en.wikipedia.org/wiki/Rechargeable_battery
https://slideplayer.com/slide/3425797/
https://pubs.acs.org/doi/abs/10.1021/ac60302a045?journalCode=ancham.
https://learn.sparkfun.com/tutorials/what-is-a-battery/all.
https://searchmobilecomputing.techtarget.com/definition/battery.
https://pubs.acs.org/doi/abs/10.1021/ac60302a045?journalCode=ancham.

## Slide 17
THANK YOU
For queries
Email: manjeet.e7825@cumail.in